## Slide 1: C H A P T E R 20 Electric Circuits

## Slide 2: Electrical Devices
Look around you. Chances are that there is an electrical device nearby - a cell phone, a computer, a projector - something that needs electrical energy to operate.

## Slide 3: CD- Player

## Slide 4: Typical Batteries and the Symbol Used to Represent Them in Electric Circuits

## Slide 5: Electromotive Force (emf)
The energy needed to run a CD player, for instance, comes from batteries.
Within a battery, a chemical reaction occurs that transfers electrons from one terminal (leaving it positively charged) to another terminal (leaving it negatively charged).
Because of the positive and negative charges on the battery terminals, an electric potential difference exists between them. The maximum potential difference is called the electromotive force* (emf) of the battery.
The electric potential difference is also known as the voltage, V.
The SI unit for voltage is the volt, after Alessandro Volta (1745-1827) who invented the electric battery. 1 volt = 1 J/C.

## Slide 6: Emf’s or Voltages of Common Batteries
Car battery = 12 V
AAA, AA, C, D = 1.5 V
9-volt battery = 9 V
Lantern battery = 6 V

## Slide 7: Electric Current
The electric current is the amount of charge per unit time that passes through a surface that is perpendicular to the motion of the charges.
The SI unit of electric current is the ampere (A), after the French mathematician André Ampére (1775-1836). 1 A = 1 C/s. Ampere is a large unit for current. In practice milliampere (mA) and microampere (μA) are used.

## Slide 8: Direction of Current Flow
Electric current is a flow of electrons. In a circuit, electrons actually flow through the metal wires.
Conventional electric current is defined using the flow of positive charges.
It is customary to use a conventional current I in the opposite direction to the electron flow.

## Slide 9: AC and DC
If the charges move around a circuit in the same direction at all times, the current is said to be direct current (dc), which is the kind produced by batteries.
In contrast, the current is said to be alternating current (ac) when the charges move first one way and then the opposite way, changing direction from moment to moment. Outlets give us ac voltage.

## Slide 10: Electrical Resistance
When electric current flows through a metal wire there exists a hindrance to the flow, known as electrical resistance.
This is because as the electrons move through they will collide with the atoms of the conductor.
The SI unit of resistance is the ohm (Ω), after Georg Simon Ohm (1787-1854), a German physicist, who discovered Ohm’s law, which will be discussed in the next section.
A resistor is a material that provides a specified resistance in an electric circuit.

## Slide 11: Ohm’s Law

## Slide 12: Ohm’s Law
Georg Simon Ohm (1787-1854), a German physicist, discovered Ohm’s law in 1826.
This is an experimental law, valid for both alternating current (ac) and direct current (dc) circuits.
When you pass an electric current (I) through a resistance (R) there will be a potential difference or voltage (V) created across the resistance.
Ohm’s law gives a relationship between the voltage (V), current (I), and resistance (R) as follows:
V = I R

## Slide 13: Units
Quantity | Symbol | Unit Name | Unit Abbreviation
Current | I | ampere | A
Voltage | V | volt | V
Resistance | R | ohm | Ω

## Slide 14: Flashlight

## Slide 15: Resistance,R and Resistivity,ρ
The resistance of a conductor is directly proportional to the length since the current needs to pass through all the atoms in the length.
The resistance is inversely proportional to the cross-sectional area since there is more room for the current to pass through.
The above observations can be combined and the resistance, R of the conductor is written as follows,

## Slide 16: Resistivity of Materials
Resistivity is an inherent property of a material, inherent in the same sense that density is an inherent property.

## Slide 17: Impedance plethysmography
In the technique of impedance plethysmography, the electrical resistance of the calf is measured to diagnose deep venous thrombosis (blood clotting in the veins).

## Slide 18: Electrical Energy
Our daily life depends on electrical energy.
We use many electrical devices that transform electrical energy into other forms of energy.
For example, a light bulb transforms electrical energy into light and heat.
Electrical devices have various power requirements.

## Slide 19: Electric Power,P
Since the electrical energy is charge times voltage (QV), the above equation becomes,
Since the current is charge flow per unit time (Q/t), the above equation becomes,
Since V = IR, the above equation can also be written as,
SI Unit of Power: watt(W)

## Slide 20: Killowatt-hour (kWh)
The SI unit of power is watt, after James Watt (1736-1819), who developed steam engines.
Utility companies use the unit kilowatt-hour to measure the electrical energy used by customers. One kilowatt-hour, kWh is the energy consumed for one hour at a power rate of 1 kW.

## Slide 21: 20.5 Alternating Current

## Slide 22: V = V 0 sin 2  f t

## Slide 23: Alternating Voltage from the outlet
Effective voltage ≈ 115 V, called the RMS value.

## Slide 24: RMS values