## Slide 1: Chapter 9
Solids and Fluids

## Slide 2: States of Matter
Solid
Liquid
Gas
Plasma

## Slide 3: Solids
Have definite volume
Have definite shape
Molecules are held in specific locations
  By electrical forces
Vibrate about equilibrium positions
Can be modeled as springs connecting molecules

## Slide 4: More About Solids
External forces can be applied to the solid and compress the material
  In the model, the springs would be compressed
When the force is removed, the solid returns to its original shape and size
  This property is called elasticity

## Slide 5: Crystalline Solid
Atoms have an ordered structure
This example is salt
  Gray spheres represent Na+ ions
  Green spheres represent Cl- ions

## Slide 6: Amorphous Solid
Atoms are arranged almost randomly
Examples include glass

## Slide 7: Liquid
Has a definite volume
No definite shape
Exists at a higher temperature than solids
The molecules “wander” through the liquid in a random fashion
  The intermolecular forces are not strong enough to keep the molecules in a fixed position

## Slide 8: Gas
Has no definite volume
Has no definite shape
Molecules are in constant random motion
The molecules exert only weak forces on each other
Average distance between molecules is large compared to the size of the molecules

## Slide 9: Plasma
Gas heated to a very high temperature
Many of the electrons are freed from the nucleus
Result is a collection of free, electrically charged ions
Plasmas exist inside stars

## Slide 10: Types of Matter
Normal matter
  About 5% of total matter
Dark matter
  Affects the motion of stars in galaxies
  May be as much at 25% of total matter
Dark energy
  Accounts for acceleration of the expansion of the universe
  May be as much as 70% of all matter

## Slide 11: Deformation of Solids
All objects are deformable
It is possible to change the shape or size (or both) of an object through the application of external forces
When the forces are removed, the object tends to its original shape
  An object undergoing this type of deformation exhibits elastic behavior

## Slide 12: Elastic Properties
Stress is the force per unit area causing the deformation
Strain is a measure of the amount of deformation
The elastic modulus is the constant of proportionality between stress and strain
  For sufficiently small stresses, the stress is directly proportional to the strain
  The constant of proportionality depends on the material being deformed and the nature of the deformation

## Slide 13: Elastic Modulus
The elastic modulus can be thought of as the stiffness of the material
  A material with a large elastic modulus is very stiff and difficult to deform
    Analogous to the spring constant

## Slide 14: Young’s Modulus: Elasticity in Length
Tensile stress is the ratio of the external force to the cross-sectional area
  Tensile is because the bar is under tension
The elastic modulus is called Young’s modulus

## Slide 15: Young’s Modulus, cont.
SI units of stress are Pascals, Pa
  1 Pa = 1 N/m2
The tensile strain is the ratio of the change in length to the original length
  Strain is dimensionless

## Slide 16: Young’s Modulus, final
Young’s modulus applies to a stress of either tension or compression
It is possible to exceed the elastic limit of the material
  No longer directly proportional
  Ordinarily does not return to its original length

## Slide 17: Breaking
If stress continues, it surpasses its ultimate strength
  The ultimate strength is the greatest stress the object can withstand without breaking
The breaking point
  For a brittle material, the breaking point is just beyond its ultimate strength
  For a ductile material, after passing the ultimate strength the material thins and stretches at a lower stress level before breaking

## Slide 18: Shear Modulus: Elasticity of Shape
Forces may be parallel to one of the object’s faces
The stress is called a shear stress
The shear strain is the ratio of the horizontal displacement and the height of the object
The shear modulus is S

## Slide 19: Shear Modulus, Equations
S is the shear modulus
A material having a large shear modulus is difficult to bend

## Slide 20: Shear Modulus, final
There is no volume change in this type of deformation
Remember the force is parallel to the cross-sectional area
  In tensile stress, the force is perpendicular to the cross-sectional area

## Slide 21: Bulk Modulus: Volume Elasticity
Bulk modulus characterizes the response of an object to uniform squeezing
  Suppose the forces are perpendicular to, and act on, all the surfaces
    Example: when an object is immersed in a fluid
The object undergoes a change in volume without a change in shape

## Slide 22: Bulk Modulus, cont.
Volume stress, ΔP, is the ratio of the force to the surface area
  This is also called the Pressure when dealing with fluids
The volume strain is equal to the ratio of the change in volume to the original volume

## Slide 23: Bulk Modulus, final
A material with a large bulk modulus is difficult to compress
The negative sign is included since an increase in pressure will produce a decrease in volume
  B is always positive
The compressibility is the reciprocal of the bulk modulus

## Slide 24: Notes on Moduli
Solids have Young’s, Bulk, and Shear moduli
Liquids have only bulk moduli, they will not undergo a shearing or tensile stress
  The liquid would flow instead

## Slide 25: Ultimate Strength of Materials
The ultimate strength of a material is the maximum force per unit area the material can withstand before it breaks or factures
Some materials are stronger in compression than in tension

## Slide 26: Post and Beam Arches
A horizontal beam is supported by two columns
Used in Greek temples
Columns are closely spaced
  Limited length of available stones
  Low ultimate tensile strength of sagging stone beams

## Slide 27: Semicircular Arch
Developed by the Romans
Allows a wide roof span on narrow supporting columns
Stability depends upon the compression of the wedge-shaped stones

## Slide 28: Gothic Arch
First used in Europe in the 12th century
Extremely high
The flying buttresses are needed to prevent the spreading of the arch supported by the tall, narrow columns

## Slide 29: Density
The density of a substance of uniform composition is defined as its mass per unit volume:
Units are kg/m3 (SI) or g/cm3 (cgs)
1 g/cm3 = 1000 kg/m3

## Slide 30: Density, cont.
The densities of most liquids and solids vary slightly with changes in temperature and pressure
Densities of gases vary greatly with changes in temperature and pressure
The higher normal densities of solids and liquids compared to gases implies that the average spacing between molecules in a gas is about 10 times greater than the solid or liquid

## Slide 31: Specific Gravity
The specific gravity of a substance is the ratio of its density to the density of water at 4° C
  The density of water at 4° C is 1000 kg/m3
Specific gravity is a unitless ratio

## Slide 32: Pressure
The force exerted by a fluid on a submerged object at any point is perpendicular to the surface of the object

## Slide 33: Measuring Pressure
The spring is calibrated by a known force
The force the fluid exerts on the piston is then measured

## Slide 34: Variation of Pressure with Depth
If a fluid is at rest in a container, all portions of the fluid must be in static equilibrium
All points at the same depth must be at the same pressure
  Otherwise, the fluid would not be in equilibrium
  The fluid would flow from the higher pressure region to the lower pressure region

## Slide 35: Pressure and Depth
Examine the darker region, assumed to be a fluid
  It has a cross-sectional area A
  Extends to a depth h below the surface
Three external forces act on the region

## Slide 36: Pressure and Depth equation
Po is normal atmospheric pressure
  1.013 x 105 Pa = 14.7 lb/in.2
The pressure does not depend upon the shape of the container

## Slide 37: Pascal’s Principle
A change in pressure applied to an enclosed fluid is transmitted undimished to every point of the fluid and to the walls of the container.
  First recognized by Blaise Pascal, a French scientist (1623 – 1662)

## Slide 38: Pascal’s Principle, cont
The hydraulic press is an important application of Pascal’s Principle
Also used in hydraulic brakes, forklifts, car lifts, etc.

## Slide 39: Absolute vs. Gauge Pressure
The pressure P is called the absolute pressure
  Remember, P = Po + gh
P – Po = gh is the gauge pressure

## Slide 40: Pressure Measurements: Manometer
One end of the U-shaped tube is open to the atmosphere
The other end is connected to the pressure to be measured
If P in the system is greater than atmospheric pressure, h is positive
  If less, then h is negative

## Slide 41: Pressure Measurements: Barometer
Invented by Torricelli (1608 – 1647)
A long closed tube is filled with mercury and inverted in a dish of mercury
Measures atmospheric pressure as ρgh

## Slide 42: Blood Pressure
Blood pressure is measured with a special type of manometer called a sphygmomano-meter
Pressure is measured in mm of mercury

## Slide 43: Pressure Values in Various Units
One atmosphere of pressure is defined as the pressure equivalent to a column of mercury exactly 0.76 m tall at 0o C where g = 9.806 65 m/s2
One atmosphere (1 atm) =
  76.0 cm of mercury
  1.013 x 105 Pa
  14.7 lb/in2

## Slide 44: Archimedes
287 – 212 BC
Greek mathematician, physicist, and engineer
Buoyant force
Inventor

## Slide 45: Archimedes' Principle
Any object completely or partially submerged in a fluid is buoyed up by a force whose magnitude is equal to the weight of the fluid displaced by the object

## Slide 46: Buoyant Force
The upward force is called the buoyant force
The physical cause of the buoyant force is the pressure difference between the top and the bottom of the object

## Slide 47: Buoyant Force, cont.
The magnitude of the buoyant force always equals the weight of the displaced fluid
The buoyant force is the same for a totally submerged object of any size, shape, or density

## Slide 48: Buoyant Force, final
The buoyant force is exerted by the fluid
Whether an object sinks or floats depends on the relationship between the buoyant force and the weight

## Slide 49: Archimedes’ Principle: Totally Submerged Object
The upward buoyant force is B=ρfluidgobjV
The downward gravitational force is w=mg=ρobjgobjV
The net force is B-w=(ρfluid-ρobj)gobjV

## Slide 50: Totally Submerged Object
The object is less dense than the fluid
The object experiences a net upward force

## Slide 51: Totally Submerged Object, 2
The object is more dense than the fluid
The net force is downward
The object accelerates downward

## Slide 52: Archimedes’ Principle: Floating Object
The object is in static equilibrium
The upward buoyant force is balanced by the downward force of gravity
Volume of the fluid displaced corresponds to the volume of the object beneath the fluid level

## Slide 53: Archimedes’ Principle: Floating Object, cont
The forces balance
  Neglects the buoyant force of the air

## Slide 54: Fluids in Motion: Streamline Flow
Streamline flow
  Every particle that passes a particular point moves exactly along the smooth path followed by particles that passed the point earlier
  Also called laminar flow
Streamline is the path
  Different streamlines cannot cross each other
  The streamline at any point coincides with the direction of fluid velocity at that point

## Slide 55: Streamline Flow, Example
Streamline flow shown around an auto in a wind tunnel

## Slide 56: Fluids in Motion: Turbulent Flow
The flow becomes irregular
  Exceeds a certain velocity
  Any condition that causes abrupt changes in velocity
Eddy currents are a characteristic of turbulent flow

## Slide 57: Turbulent Flow, Example
The rotating blade (dark area) forms a vortex in heated air
  The wick of the burner is at the bottom
Turbulent air flow occurs on both sides of the blade

## Slide 58: Fluid Flow: Viscosity
Viscosity is the degree of internal friction in the fluid
The internal friction is associated with the resistance between two adjacent layers of the fluid moving relative to each other

## Slide 59: Characteristics of an Ideal Fluid
The fluid is nonviscous
  There is no internal friction between adjacent layers
The fluid is incompressible
  Its density is constant
The fluid motion is steady
  Its velocity, density, and pressure do not change in time
The fluid moves without turbulence
  No eddy currents are present
  The elements have zero angular velocity about its center

## Slide 60: Equation of Continuity
A1v1 = A2v2
The product of the cross-sectional area of a pipe and the fluid speed is a constant
  Speed is high where the pipe is narrow and speed is low where the pipe has a large diameter
Av is called the flow rate

## Slide 61: Equation of Continuity, cont
The equation is a consequence of conservation of mass and a steady flow
A v = constant
  This is equivalent to the fact that the volume of fluid that enters one end of the tube in a given time interval equals the volume of fluid leaving the tube in the same interval
    Assumes the fluid is incompressible and there are no leaks

## Slide 62: Daniel Bernoulli
1700 – 1782
Swiss physicist and mathematician
Wrote Hydrodynamica
Also did work that was the beginning of the kinetic theory of gases

## Slide 63: Bernoulli’s Equation
Relates pressure to fluid speed and elevation
Bernoulli’s equation is a consequence of Conservation of Energy applied to an ideal fluid
Assumes the fluid is incompressible and nonviscous, and flows in a nonturbulent, steady-state manner

## Slide 64: Bernoulli’s Equation, cont.
States that the sum of the pressure, kinetic energy per unit volume, and the potential energy per unit volume has the same value at all points along a streamline

## Slide 65: Applications of Bernoulli’s Principle: Measuring Speed
Shows fluid flowing through a horizontal constricted pipe
Speed changes as diameter changes
Can be used to measure the speed of the fluid flow
Swiftly moving fluids exert less pressure than do slowly moving fluids

## Slide 66: Applications of Bernoulli’s Principle: Venturi Tube
The height is higher in the constricted area of the tube
This indicates that the pressure is lower

## Slide 67: An Object Moving Through a Fluid
Many common phenomena can be explained by Bernoulli’s equation
  At least partially
In general, an object moving through a fluid is acted upon by a net upward force as the result of any effect that causes the fluid to change its direction as it flows past the object
Swiftly moving fluids exert less pressure than do slowing moving fluids

## Slide 68: Application – Golf Ball
The dimples in the golf ball help move air along its surface
The ball pushes the air down
Newton’s Third Law tells us the air must push up on the ball
The spinning ball travels farther than if it were not spinning

## Slide 69: Application – Airplane Wing
The air speed above the wing is greater than the speed below
The air pressure above the wing is less than the air pressure below
There is a net upward force
  Called lift
Other factors are also involved

## Slide 70: Surface Tension
Net force on molecule A is zero
  Pulled equally in all directions
Net force on B is not zero
  No molecules above to act on it
  Pulled toward the interior of the fluid

## Slide 71: Surface Tension, cont
The net effect of this pull on all the surface molecules is to make the surface of the liquid contract
Makes the surface area of the liquid as small as possible
  Example: Water droplets take on a spherical shape since a sphere has the smallest surface area for a given volume

## Slide 72: Surface Tension on a Needle
Surface tension allows the needle to float, even though the density of the steel in the needle is much higher than the density of the water
The needle actually rests in a small depression in the liquid surface
The vertical components of the force balance the weight

## Slide 73: Surface Tension, Equation
The surface tension is defined as the ratio of the magnitude of the surface tension force to the length along which the force acts:
SI units are N/m
In terms of energy, any equilibrium configuration of an object is one in which the energy is a minimum

## Slide 74: Measuring Surface Tension
The force is measured just as the ring breaks free from the film
  The 2L is due to the force being exerted on the inside and outside of the ring

## Slide 75: Final Notes About Surface Tension
The surface tension of liquids decreases with increasing temperature
Surface tension can be decreased by adding ingredients called surfactants to a liquid
  Detergent is an example

## Slide 76: A Closer Look at the Surface of Liquids
Cohesive forces are forces between like molecules
Adhesive forces are forces between unlike molecules
The shape of the surface depends upon the relative size of the cohesive and adhesive forces

## Slide 77: Liquids in Contact with a Solid Surface – Case 1
The adhesive forces are greater than the cohesive forces
The liquid clings to the walls of the container
The liquid “wets” the surface

## Slide 78: Liquids in Contact with a Solid Surface – Case 2
Cohesive forces are greater than the adhesive forces
The liquid curves downward
The liquid does not “wet” the surface

## Slide 79: Contact Angle
In a, Φ > 90° and cohesive forces are greater than adhesive forces
In b, Φ < 90° and adhesive forces are greater than cohesive forces

## Slide 80: Capillary Action
Capillary action is the result of surface tension and adhesive forces
The liquid rises in the tube when adhesive forces are greater than cohesive forces
At the point of contact between the liquid and the solid, the upward forces are as shown in the diagram

## Slide 81: Capillary Action, cont.
Here, the cohesive forces are greater than the adhesive forces
The level of the fluid in the tube will be below the surface of the surrounding fluid

## Slide 82: Capillary Action, final
The height to which the fluid is drawn into the tube is given by:

## Slide 83: Viscous Fluid Flow
Viscosity refers to friction between the layers
Layers in a viscous fluid have different velocities
The velocity is greatest at the center
Cohesive forces between the fluid and the walls slow down the fluid on the outside

## Slide 84: Coefficient of Viscosity
Assume a fluid between two solid surfaces
A force is required to move the upper surface
η is the coefficient
SI units are N . s/m2
cgs units are Poise
  1 Poise = 0.1 N.s/m2

## Slide 85: Poiseuille’s Law
Gives the rate of flow of a fluid in a tube with pressure differences

## Slide 86: Reynold’s Number
At sufficiently high velocity, a fluid flow can change from streamline to turbulent flow
  The onset of turbulence can be found by a factor called the Reynold’s Number, RN
  If RN = 2000 or below, flow is streamline
  If 2000 <RN<3000, the flow is unstable
  If RN = 3000 or above, the flow is turbulent

## Slide 87: Transport Phenomena
Movement of a fluid may be due to differences in concentration
  As opposed to movement due to a pressure difference
  Concentration is the number of molecules per unit volume
The fluid will flow from an area of high concentration to an area of low concentration
The processes are called diffusion and osmosis

## Slide 88: Diffusion and Fick’s Law
Molecules move from a region of high concentration to a region of low concentration
Basic equation for diffusion is given by Fick’s Law
D is the diffusion coefficient

## Slide 89: Diffusion
Concentration on the left is higher than on the right of the imaginary barrier
Many of the molecules on the left can pass to the right, but few can pass from right to left
There is a net movement from the higher concentration to the lower concentration

## Slide 90: Osmosis
Osmosis is the movement of water from a region where its concentration is high, across a selectively permeable membrane, into a region where its concentration is lower
  A selectively permeable membrane is one that allows passage of some molecules, but not others

## Slide 91: Motion Through a Viscous Medium
When an object falls through a fluid, a viscous drag acts on it
The resistive force on a small, spherical object of radius r falling through a viscous fluid is given by Stoke’s Law:

## Slide 92: Motion in a Viscous Medium
As the object falls, three forces act on the object
As its speed increases, so does the resistive force
At a particular speed, called the terminal speed, the net force is zero

## Slide 93: Terminal Velocity, General
Stokes’ Law will not work if the object is not spherical
Assume the resistive force has a magnitude given by Fr = k v
  k is a coefficient to be determined experimentally
The terminal velocity will become

## Slide 94: Sedimentation Rate
The speed at which materials fall through a fluid is called the sedimentation rate
  It is important in clinical analysis
The rate can be increased by increasing the effective value of g
  This can be done in a centrifuge

## Slide 95: Centrifuge
High angular speeds give the particles a large radial acceleration
  Much greater than g
  In the equation, g is replaced with 2r

## Slide 96: Centrifuge, cont
The particles’ terminal velocity will become
The particles with greatest mass will have the greatest terminal velocity
The most massive particles will settle out on the bottom of the test tube first